## Slide 1
JAPAN
Takeyasu Sakai
GNSS Implementation Team

## Slide 2
Presented by:
Takeyasu Sakai
National Institute of Maritime, Port and Aviation Technology, Japan
Agenda 9: Update on Satellite Constellations and Plans
Status of Japanese QZSS and SBAS Programs

## Slide 3
QZSS (Quasi-Zenith Satellite System) Program
  Regional navigation service broadcast from high-elevation angle by a combination of three satellites on the inclined geosynchronous (quasi-zenith) orbit and a GEO.
  The first satellite “Michibiki” launched in 2010 has been continuously broadcasting GPS-like ranging signals and some augmentation signals.
  Begins the operation with 4-satellite constellation in April 2018, and 7-satellite constellation will follow in 2023.
  The mission of the operational QZSS:
    Positioning: Ranging and augmentation services including SBAS; and
    Messaging: Two-way mobile communication service for disaster and crisis management.
MSAS: Japanese SBAS Service
  Operational since 2007 in accordance with the ICAO standards.
  Continues operation with MTSAT-2 GEO.
    Replacement to the fully new system and new GEO in 2020;
    Integrated to the QZSS program.
    Upgrade for vertical guidance likely in 2023 with the 2nd GEO.
Introduction

## Slide 4
Part I
Status of the QZSS Program

## Slide 5
QZSS Concept
Broadcast signal from high elevation angle.
Applicable to navigation services for mountain area and urban canyon.
Augmentation signal from the zenith could help users to acquire and augment other GNSS satellite signals at any time.
IGSO (Inclined Geosynchronous Orbit) centered at 139E.
Eccentricity 0.075, inclination 41deg.
Additional GEO.
QZSS-IGSO
GPS/GEO
GEO
IGSOs

## Slide 6
Mission
Mission 1: Positioning Services
  Ranging Service:
    Broadcasts GPS-like ranging signals on three frequencies (L1C/A, L2C, L5I/Q, and L1C) to improve availability of navigation in urban and mountain areas.
  Submeter Level Augmentation Service:
    SLAS on L1S
    Code-phase differential correction
    service for mobile users.
  Centimeter Level Augmentation Service:
    CLAS on L6D
    Carrier-phase differential correction
    service for precision applications.
Mission 2: Messaging Service
  Provides two-way mobile communication
  service for disaster and crisis management.
  Downlink short messages on L1 frequency.
  S-band two-way communication for emergency safety report.
QZSS
Orbit and Ground Track
(C)JAXA

## Slide 7
4-Satellite Constellation in 2020
Equator
QZS Visibility from Japan
・ 2 to 3 IGSOs above 20 deg. elevation;
・ At least 1 IGSO above 60 deg. elevation.
Now we have the QZS-1 satellite on orbit.
Three additional satellites will be launched by mid-2017; 2 IGSO and 1 GEO.
Contour of QZSS Minimum Elevation Angle
Quasi-Zenith Orbit (IGSO)
GEO @127E
・ Improved visibility
・ Additional services

## Slide 8
QZSS Ranging Signals
Signal | Frequency MHz | Service | Compatibility | QZS-1 | QZS-2/4 | QZS-3
 |  |  |  | IGSO | IGSO | GEO
L1C/A | 1575.42 | Positioning | Complement GPS |  |  | 
L1C |  | Positioning | Complement GPS |  |  | 
L1S |  | Augmentation (SLAS) | QZSS Service |  |  | 
 |  | Messaging | QZSS Service |  |  | 
L1Sb |  | Augmentation (SBAS) | SBAS (L1) Service | — | — | 
L2C | 1227.60 | Positioning | Complement GPS |  |  | 
L5 I/Q | 1176.45 | Positioning | Complement GPS |  |  | 
L5S |  | Experimental Use (L5 SBAS) | SBAS (L5) Service | — |  | 
L6D (D1) | 1278.75 | Augmentation (CLAS) | QZSS Service |  |  | 
L6E (D2) |  | Experimental Use (MADOCA) | QZSS Service | — |  | 

## Slide 9
Organization
Government of Japan
Office of National Space Policy
Cabinet Office
QZS System Service Inc. (QSS)
NEC Corp.
(NEC)
Mitsubishi Electric Corp. (MELCO)
QZSS Project
Contract (PFI)
System and Service
Provision
Contract for Ground
System Procurement
System Developers
Contract for satellites
SBAS Project
Ministry of Land, Infrastructure, Transport and Tourism
Civil Aviation Bureau of Japan(JCAB)
SBAS Facility
I/F: Data and operational information

## Slide 10
Near-Term Plan
Fiscal Year | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 and Later
1st Michibiki |  |  |  |  |  |  |  |  | 
QZSS 4-Satellite Constellation |  |  |  |  |  |  |  |  | 
QZSS 7-Satellite Constellation |  |  |  |  |  |  |  |  | 
Service
Development/Launch (Additional 3 satellites)
Service
Experiment/Test
Replenish Satellite
Launch #1-R
Launch #2,3,4
SBAS Service

## Slide 11
QZSS Satellites #2 and #4
139 degree
Satellite #2 Launch: June 1, 2017.

## Slide 12
QZSS Satellite #3 (GEO)
Additional S-band antenna for two-way communication for emergency safety report.
L1b signal for SBAS service.

## Slide 13
QZSS Master Stations
QZSS Control Center
Kobe (Backup)
QZSS Control Center
Hitachi-Ota (Primary)

## Slide 14
QZSS TTC Stations
7 TTC (Telemetry, Tracking, and Command) stations: Most are at the southern part of Japan for satellite visibility.
All TTC stations were built and set operational by the end of 2016.
Master
Stations

## Slide 15
QZSS Monitor Stations

## Slide 16
QZS-1 Signal Quality
(Courtesy: (c) JAXA)
Since June, 2011, QZSS have provided navigation signals with good qualities, satisfying with their performance specifications, continuously.
  For this month
  of January 2017,
  SIS-URE was just
  0.315m RMS.
10 m
Specification on SIS-URE = 2.6m (95%)
2017/01/01
2017/01/11
2017/01/21
2017/01/31
5
4
3
2
1
0
-1
-2
-3
-4
-5
Average -0.065 [m]
RMS 0.315 [m]
Percentage of time (|URE| ≦2.6 [m]) 100.0%
{Spec: ≧95%}
SIS-URE of QZS-1 L1C/A is 0.4m RMS level
Comparable to those for GPS Block IIRM and IIF satellites

## Slide 17
Part II
MSAS: Japanese SBAS Program

## Slide 18
MSAS Program
Beginning of SBAS Program in Japan:
  JCAB (Japan Civil Aviation Bureau) of Ministry of Land, Infrastructure, Transport and Tourism decided the development of its own SBAS in 1993.
  The system named MSAS, or MTSAT Satellite-based Augmentation System, was originally planned to be operational in 2000.
MSAS GEO Satellites:
  MTSAT (Multi-functional Transport Satellite): Aviation and weather missions.
    MTSAT works for AMSS and SBAS services for aviation.
  Launch of the MTSAT-1 was unfortunately failed in 1999.
    Spare satellite: MTSAT-1R was launched in February 2005.
  2nd GEO: MTSAT-2 on the orbit in February 2006.
Ground facilities:
  Consists of 2 MCS (KASC and HASC), 6 GMS, and 2 MRS.
Beginning Operation:
  Broadcast test signal since summer 2005.
  Finally, MSAS began its operation in September 27, 2007 after certification.

## Slide 19
MRJ (Courtesy: MHI)
Current Status
MSAS: Japanese SBAS in operation.
  Operational since Sept. 27, 2007.
  Continue operation with 2 signals via 1 GEO.
    MTSAT-1R decommissioned in Dec. 2015.
    Hawaii and Australia MRS sites are
    removed in Feb. 2015.
Service for Air Navigation
  GPS Augmentation Information for RNAV,
  from En-route through NPA (RNP 0.3 performance).
    Within Fukuoka FIR.
    Only horizontal navigation due to ionosphere activities.
  NOTAM is available to MSAS users.
    Alert for Service Interruption.
    Alert for Predicted Service Outage.
Expanding Users
  Most small/regional jets equip SBAS-capable avionics.
  Japanese new regional jet, MRJ will also be capable of SBAS.
(c) Mitsubishi Electric Corp.
MSAS GEO: MTSAT-2

## Slide 20
Current Configuration
MSAS Monitor Stations
Ranging Signals
GPS Satellites
Ground
Network
Naha GMS
Fukuoka GMS
Tokyo
GMS
Sapporo
GMS
Hitachi-Ota MCS
(and GMS)
Kobe MCS
(and GMS)
Users
MTSAT-2
Augmentation Signals
PRN129
PRN137
6 GMS
in Japan
1 GEO, 2 MCS (Master Control Station) and 6 GMS (Ground Monitor Station);
MTSAT-2 is broadcasting 2 signals from 2 MCS (PRN129 and PRN137);
Remote sites in Hawaii and Australia were removed from the original configuration.

## Slide 21
Correction Performance
GEONET 940058 (Takayama) 16/8/8-12 (5 days)
PRN129 and PRN137 Broadcast Signal
GPS only
MSAS PRN129
Horizontal
0.722m RMS
GPS only
MSAS PRN137
Horizontal
0.717m RMS

## Slide 22
Integrity Performance
Actual Error, m
Horizontal Protection Level (HPL), m
HAL=556m
Loss of Availability
Normal
Operation
Loss of
Availability
& Integrity
Loss of
Integrity
Loss of
Integrity
2016/4/19 Ishigaki Island MTSAT PRN137 Horizontal Error and Protection Level

## Slide 23
Continuous Operation
Current status:
  MTSAT-1R decommissioned in 2015. MTSAT-2 will be in 2020.
  2 MRS sites removed in 2015.
  The ground facilities need to be upgraded: It is difficult to maintain 20-year old equipment.
Replacement in 2020:
  MSAS V1 continues operation with a GEO (MTSAT-2) and 6 GMS by 2020.
    Decommission of MTSAT-2 planned in 2020.
  In 2020, MSAS V2 takes over the operation with a new GEO.
    Integrated to the QZSS program.
    The L1Sb signal of QZS-3 (GEO) will be used for MSAS service.
  MCS equipment will also be fully replaced at the same time.
  7 GMS will be added: Totally 13 GMS domestic.
  Performance will be similar with the current MSAS: Horizontal only.

## Slide 24
Improvement Plan
Supporting vertical guidance: MSAS V2.1
  Vertical guidance: LPV operation.
  Need software upgrade:
    Adding GMS cannot overcome ionospheric effects.
    ENRI has been developed the improved algorithms for ionospheric correction.
  Will be supported in accordance with introduction of the 2nd GEO in 2023.
Dual-Frequency operation: MSAS V3
  Eliminates ionospheric effects dramatically.
    Robust vertical guidance (LPV and LPV-200) in the whole Japanese airspace.
  QZSS GEO will have the L5S signal useable for DFMC SBAS.
    DFMC: Dual-Frequency Multi-Constellation
  ENRI will begin DFMC SBAS experiment in 2018 with QZSS satellites.
    Early opportunity of the DFMC SBAS real signal from the space.
    Initial test by mid-2017 following launch of QZS-2 IGSO.
    Expects participation to this experiments from Asia Pacific Economies.

## Slide 25
Prototype DFMC SBAS
Dual Frequency
DFMC L5 SBAS
Location:
GEONET 950369
(Wakayama)
Period:
2016/12/15 (24H)
SBAS corrections improve position accuracy in both modes of GPS and GPS+GLONASS.
SBAS messages are generated by the prototype DFMC SBAS developed
by ENRI, in accordance with the draft DFMC L5 SBAS standards.

## Slide 26
MSAS Evolution Plan
DFMC SBAS trial begins in 2018; Initial test by mid-2017.
Replacement to the new QZSS-based system in 2020.
LPV/LPV-200 upgrade likely in 2023 and DFMC SBAS implementation after that.

## Slide 27
Conclusion
QZSS: Japanese Regional Satellite Navigation System
  Services: GPS-complement ranging, GNSS augmentation, and Messaging.
  4-satellite constellation including 3 IGSO and a GEO in 2018.
  Will be extended to 7-satellite constellation by 2023.
MSAS: Japanese SBAS Service
  An operational SBAS in accordance with the ICAO standards.
  Current service: Horizontal navigation (Enroute to NPA performance).
  Evolution plan:
    MSAS V2: Replacement to the fully new system and new GEO in 2020.
    MSAS V2.1: Upgrade for vertical guidance likely in 2023 with the 2nd GEO; Supporting LPV operations.
    Dual-frequency Multi-Constellation L5 SBAS trial since 2018 with real signals towards MSAS V3; Initial test by mid-2017.
Contact for more information:
Dr. Takeyasu Sakai <sakai@mpat.go.jp>
Electronic Navigation Research Institute
National Institute of Maritime, Port and Aviation Technology, Japan